## Slide 1
Ivan Bereziuk (group: LC) supervisor: S. Riemann, F. Staufenbiel
the project ILC
The positron production target
Material science
Dynamical and static stress calculations
Temperature distribution in a test target

## Slide 2
We work for the project ILC:

## Slide 3
The positron production target
r = 1 m
vrim = 100 m/s
2*1010 e- / bunch = 3.2 nC / bunch
2625 bunch / train (0.97ms)
5 train / s
-> 4.6*1015 photon / train
~ 14.4 MeV e+
Titan target for polarised positron production
r
250 GeV e-
helical undulator
~ 28.8 MeV photon beam
distribution of
heat load !!

## Slide 4
This simple geometry of this test target is fixed. The dynamical evolution is studied by rapidly pulsed heating. The original target is a rotating wheel and it`s modeling is the next step of the research.
Оur goal: to check target properties and the limits for break down by using ANSYS - software. That is used to solve the problems of time dependent stress (velocity) evolution , deformation ...
Basic research in ANSYS scheme is as follows:
Geometry Meshing Heating Stress analysis
The question and method of solving

## Slide 5
Thomas Young (* 1773 +1829)
Robert Hooke (* 1635 +1703)
E =
Ds
De
Material science

## Slide 6: - fixed titanium rectangular target for dynamical studies - gamma rays penetrates it`s and electron-positron pairs are produced - the heat loads is simulated via FLUKA Monte Carlo code
28.8 MeV photon beam
Temperature distribution in a test target

## Slide 7
Fatigue stress (Ti) < 400 MPa
upper limit of renewable strain(elastic) = 800 MPa
Dynamical stress evolution in a test target

## Slide 8
Dynamic
Static
The stress maximum is induced by wave superposition. The maximum of the stress area is close to the center of body but not on in the maximal heated area of the target. The static stress value is about 50 MPa. This is a factor of 4 less than in the case of the dynamic stress evolution with value of about 200 MPa for 50 bunches at the same place.
Dynamical and static stress calculations

## Slide 9
Conclusion
The solid Ti target hitted by an intense photon beam with ILC time structure behaves like liquid material.
It seems that depending on the geometry and target material properties, the periodic heat load due to an intense beam can produce strong stress waves which easily exceed the elastic limit. It could be possible that these waves build up further and could destroy the target.

## Slide 10
Thanks for your attention!